## Slide 1: MATERIAL SYNTHESIS SQUID

## Slide 2: SQUID(Superconducting Quantum Interference Device
A SQUID (superconducting quantum interference device) is a very sensitive magnetometer used to measure extremely weak magnetic fields, based on superconducting loops containing Josephson junctions.
SQUIDs are sensitive enough to measure fields as low as 5×10−14 T.
There are two main types of SQUID they are:
direct current (DC) ,&
radio frequency (RF).

## Slide 3: Josephson Junctions
A SQUID consists of a loop with two Josephson junctions interrupting the loop.
SQUID is a mechanism for measuring extremely weak signals in Josephson junction.
The operation of a SQUID magnetometer is based on two effects flux quantization and the Josephson effect.

## Slide 4: .
The classical Josephson junction consists of an insulating barrier between two superconductors thin enough to couple “weakly.”
There are two types of SQUID, the radio frequency (RF) SQUID consisting of only one Josephson junction, and the direct current (DC) SQUID with two or more junctions.
The RF is cheaper in construction but less sensitive compared to the DC.

## Slide 5: Direct Current (DC)
we pass a constant current, known as a bias current, through the SQUID. If the SQUID is symmetrical and the junctions are identical, the bias current will split equally, half on each side.

## Slide 6: Radio Frequency (RF)
The RF (Radio Frequency) SQUID is a one-junction SQUID loop that can be used as a magnetic field detector

## Slide 7: Application
A SQUID is a very sensitive magnetometer used to measure extremely weak magnetic fields, based on superconducting loops containing Josephson junctions.
SQUIDs are sensitive enough to measure fields as low as 5×10−14 T with a few days of averaged measurements.
SQUIDs are used in superparamagnetic relaxometry (SPMR), a technology that utilizes the high magnetic field sensitivity of SQUID sensors and the superparamagnetic properties of magnetite nanoparticles.

## Slide 8: Uses
SQUID magnetometers are generally used to measure the magnetization of very small samples (e.g., thin films) or systems that are just on the limit of magnetic order.
Therefore, SQUID magnetometers are mainly applied to scientific investigations.

## Slide 9: Thankyou…